## Slide 1: R-wave detection SRS Presentation
Junwei Lin
Electrical and Computer Engineering MEng student
January 28, 2025

## Slide 2: Introduction
R-wave detection is an important task in ECG signal processing
heart rate calculation
arrhythmia analysis
heart disease diagnosis
Analog signal
Digital signal
Electric shock?
1/10

## Slide 3: Introduction
normal sinus rhythm ECG wave
Real ECG wave from MIT-BIH
2/10

## Slide 4: Challenge
3/10
Noise
Baseline shift
Premature ventricular contractions

## Slide 5: General System Description
RMSE
sampling frequency
Discrete-time ECG signal
Index of the calculated n-th R wave
Index of the annotated n-th R wave
Root Mean Square Error
4/10

## Slide 6: Goals Statement
5/10
Goal ID | Goal description
G1 | Develop an efficient algorithm that can accurately detect R waves in ECG signals
G2 | Automatically derive filter-related parameters in the G1 algorithm

## Slide 7: Assumptions
6/10
Assumption ID | Assumption description
A1 | The sampling frequency is not lower than the Nyquist frequency
A2 | The R-wave has peak characteristics that can be discerned by the naked eye.
A3 | The input ECG signal is of high quality and has no defects.
A4 | Noise in data can be filtered out, within expectations

## Slide 8: Inputs and Outputs variables
7/10
symbol | I/O | description | unit | range | Typical value
 | I | Sampling frequency | Hz | 100 Hz ~ 5000 Hz | 360 Hz
 | I | ECG signal | mV | 0 mV~10 mV | 0.5 mV ~ 3.0 mV
N | I | Length of | / | <= 1,000,000 | 36000 (360 Hz, 100 s)
 | I | Annotated data | / | <= N / 10 | depending on
 | O | Index of the calculated n-th R wave | / | <= N / 10 | depending on
RMSE | O | Root Mean Square Error | / | <= 10 | depending on and
symbol | I/O | description | unit | range | Typical value
 | I | Sampling frequency | Hz | 100 Hz ~ 5000 Hz | 360 Hz
 | I | ECG signal | mV | 0 mV~10 mV | 0.5 mV ~ 3.0 mV
N | I |  | / | <= 1,000,000 | 36000 (360 Hz, 100 s)
 | I | Annotated data | / | <= N / 10 | 
 | O | Index of the calculated n-th R wave | / | <= N / 10 | 
RMSE | O | Root Mean Square Error | / |  | 

## Slide 9: Theoretical Models
8/10
ID | description
TM1 | Equations for Digital Filters:
TM2 | Butterworth filter:
TM3 | threshold detect:
ID | description
TM1 | 
TM2 | 
TM3 | 

## Slide 10: Instanced Models
8/10
ID | description
IM1 | 11Hz Low-pass filter for removing utility frequency and noise, Ref. TM1, TM2
IM2 | 5Hz High-pass filter for removing baseline shift, Ref. TM1, TM2
IM3 | Moving window, Ref. TM1
IM4 | R-wave detect in filtered signal by flexible threshold, Ref. TM3

## Slide 11: Requirements (Not complete)
9/10
Req ID | Requirement description
R1 | Implement basic low-pass and high-pass filters using difference equations
R2 | Implement parameter derivation of widely used filters, including Butterworth, Chebyshev
R3 | Implement mathematical functions including squaring, thresholding
R4 | Combine mathematical functions and filters to calculate R-wave position
R5 | User-friendly input and output formats, and echoing the inputs as part of the output
NFR1 | Write cross-platform and portable code
NFR2 | Code needs to pass static analysis

## Slide 12: Thank you for listening. Any questions?
10/10